## Slide 1: Forward Calorimeter Prototype
Daniel Brown, for the STAR collaboration

## Slide 2: The Prototype
AGS-E864 Collaboration Lead Calorimeter from IP2
Installed for STAR Run16
Specifications
  2x3 Lead Block Stack
    10cmx10cmx117cm blocks
  Spaghetti Calorimetry
  Spatial Resolution – 54 pixels at 3.3cmx3.3cm
    9 Fresnel Lenses + Silicon Photomultiplier (SiPM)
    18 Fresnel Lenses + Photomultiplier Tube (PMT)
    27 Acrylic Light Guides + Photomultiplier Tube
  Nuclear Interaction Length – 7 Interaction Lengths
  Hadronic Resolution – 34%/Sqrt[E]

## Slide 3: The Prototype
117 cm
10 cm
10 cm
AGS-E864 Collaboration Lead Calorimeter from IP2
Installed for STAR Run16
Specifications
  2x3 Lead Block Stack
    10cmx10cmx117cm blocks
  Spaghetti Calorimetry
  Spatial Resolution – 54 pixels at 3.3cmx3.3cm
    9 Fresnel Lenses + Silicon Photomultiplier (SiPM)
    18 Fresnel Lenses + Photomultiplier Tube (PMT)
    27 Acrylic Light Guides + Photomultiplier Tube
  Nuclear Interaction Length – 7 Interaction Lengths
  Hadronic Resolution – 34%/Sqrt[E]

## Slide 4: Prototype Detector Location
North side of the east tunnel
Less iron  lower fringe field effects
FCal

## Slide 5: Prototype Goals
Reaffirming Run 14 Data
  2014 Run Data Shown – Highly Stable
  Retain Stability – “Set it and forget it”
Hardware Tests
  Mu-Metal Shielding
  Fresnel Light Guides
  Silicon Photomultipliers
Neutral Pion Finding
  Calibration
Average energy deposition per run,
for entire 200 GeV 3He+Au operation
as a function of run number, for three
selected pixels which are close to beam pipe.

## Slide 6: Mu-Metal Shielding
Magnetic field effects on photomultiplier tubes (PMTs)
  Magnetic field alters cascade in PMTs
Magnetic field shielding
  Known passive shielding
  Amount required
  Interaction with optical system
Notes: http://www.mu-metal.com/uploads/5/4/5/0/54501895/7134668.jpg
https://www.hamamatsu.com/us/en/technology/innovation/photocathode/index.html

## Slide 7: Fresnel Lens Light Guides
Alternative to acrylic light guide
Replaceable parts
  Commercial item
  Can be machined to fit
  Can be installed after stacking
Notes: Fresnel Images: http://hyperphysics.phy-astr.gsu.edu/hbase/geoopt/imggo/fresnel.gif
http://www.pnta.com/lighting/lenses/6-fresnel-lens/

## Slide 8: Fresnel Lens Light Guides
Alternative to acrylic light guide
Replaceable parts
  Commercial item
  Can be machined to fit
  Can be installed after stacking
Notes: Fresnel Images: http://hyperphysics.phy-astr.gsu.edu/hbase/geoopt/imggo/fresnel.gif
http://www.pnta.com/lighting/lenses/6-fresnel-lens/

## Slide 9: Fresnel Lens Light Guides
Alternative to acrylic light guide
Replaceable parts
  Commercial item
  Can be machined to fit
  Can be installed after stacking
Notes: Fresnel Images: http://hyperphysics.phy-astr.gsu.edu/hbase/geoopt/imggo/fresnel.gif
http://www.pnta.com/lighting/lenses/6-fresnel-lens/

## Slide 10: Silicon Photomultipliers (SiPMs)
Compared to photomultiplier tubes
  Magnetic field effects
  Lower cost
  Smaller
Stability over time
  Radiation resistance

## Slide 11: Results
Mu-Metal Shielding
  Acrylic light guides limit length
  Fits into Fresnel lens system
  8 degree tilt reduces field effects
  Optimal minimal recess of 5.8cm
  Reduces magnetic field effects to <5%
Fresnel Lens Light Guides
  Greater light levels than acrylic light guides
  More secure photomultiplier tubes
  Allows for proper recession distance

## Slide 12: Results
Silicon Photomultipliers Testing over 28 days
  Changes due to radiation – Not stable Blue: PMT
  Not suitable for this application due to placement Magenta: SiPM

## Slide 13: Results
Neutral pion finding STAR Trigger used
  Early results Au+Au Collisions used
  Used for calibration No Centrality explicitly selected
  π0  γ + γ 12% of available data used
  Further calibration needed 4 Cells of Run16 data
Pixelization

## Slide 14: Conclusions
Mu-Metal
  Provides adequate shielding
  Gain shifts reduced to <5%
  Allows use of PMTs close to the beam pipe
Fresnel Lens Light Guides
  Increase light levels
  Allows easy installation of components
  Allows easy replacement of components
  More secure PMTs
Silicon Photomultipliers
  Gain changes over time
  Not suitable
Neutral Pion Finding
  Reconstruction possible
  Used for calibration
  Further calibration needed
Results
  Results were positive
  Investigation of installation possibilities underway

## Slide 15: SiPM Test Procedure
“A blue LED is pulsed continuously at ~100 Hz. Both an xp2262 and a 36x1-mm diameter fiber bundle view the pulsed LED. The phototube is ch=2 and the SiPM array is ch=3 on the escope. A script acquires e-scope images every ~20min [I do not recall the precise "sleep" time in the script], and stamps the acquired file with UNIX time. A separate script records your readable I2C values from your SiPM FEE every ~20min, and stamps a log file with UNIX time. From that we get leakage current.”

## Slide 16: Code Conversion and Data Analysis
Finishing converting code to C++ / ROOT
  Open analysis to everyone
2016 Prototype data analysis
  Side by side comparisons
  Reaffirm 2014 data

## Slide 17: Data Acquisition
Electronics designed/built by Berkeley group
[H. Crawford, et al.] for STAR digital trigger
DAQ written for IP2 effort by C. Perkins
DAQ/digital trigger system previously used at IP2
In 2011-13. Last used at FermiLab for T1064
All items powered from 108VAC
Installed in Wide Angle Hall east side
All components remotely controlled via
CANBUS (VME) or network-power switch