## Slide 1: The STAR Heavy Flavor Tracker
Flemming Videbæk
For the STAR collaboration
Brookhaven National Lab
Notes: Add logo’s

## Slide 2: STAR HFT Upgrade Motivation
Direct topological reconstruction of Charm in STAR events
Detect charm decays with small c, including D0  K 
Separation of Charm and Bottom
Method: Resolve displaced vertices (123 m)
200 GeV Au-Au , p+p collisions @ RHIC
Notes: Highlight detecting short lived particles –
you have heard about the physics in previous talks

## Slide 3: Heavy Flavor Tracker (HFT)
TPC Volume
Magnet
Return Iron
Solenoid
EAST
WEST
FGT

## Slide 4: Heavy Flavor Tracker (HFT)
SSD
IST
PXL
HFT
Detector | Radius (cm) | Hit Resolution R/ - Z (m - m) | Radiation length
SSD | 22 | 20 / 740 | 1% X0
IST | 14 | 170 / 1800 | <1.5 %X0
PIXEL | 8 | 12/ 12 | ~0.5 %X0
 | 2.7 | 12 / 12 | ~0.5% X0
SSD
existing single layer detector, double side strips (electronic upgrade)
IST
one layer of silicon strips along beam direction, guiding tracks from the SSD through PIXEL detector.
PIXEL
two layers
20.7x20.7 m pixel pitch
10 sector, delivering ultimate pointing resolution that allows for direct topological identification of charm.
~360M pixels
monolithic active pixel sensors (MAPS) technology

## Slide 5: PXL Detector Design
Mechanical support with kinematic mounts (insertion side)
  4 ladders / sector
  5 sectors / half (10 sectors total)
  2 layers
  Insertion from one side
Cu conductor Ladder Flex Cable
Ladder with 10 MAPS sensors (~ 2×2 cm each)
carbon fiber sector tubes (~ 200 µm thick)
20 cm
Novel rapid insertion mechanism allows effective exchanges and repairs (~12 h)
Precision kinematic mount guarantees reproducibility to < 20 microns
Prototype engineering run in May with 3 sectors. (Talks by J.Bouchet & L.Ma)
Notes: What is the carbon fiber process used?

## Slide 6: Intermediate Silicon Tracker (IST)
24 ladders, liquid cooling.
Production Ladder
S:N > 20:1
>99.5% live and functioning channels
24 ladders 50 cm long
at 14 cm
Si pad detector .6*6 mm pads
36 APV hybrids per ladder for readout
Liquid cooling at 24oC
<1.5% radiation length

## Slide 7: Silicon Strip Detector (SSD)
~ 1 Meter
Ladder Cards
Existing detector
20 ladders at 22 cm
Double sided Si with total ~400k strips
New, faster readout ~15% deadtime at 1 KHz limited by original detector hybrids

## Slide 8: Support Structures
Notes: Insert picture of assemble structures/ look at pictures that Bill showed at collaboration meeting

## Slide 9: Physics of the Heavy Flavor Tracker at STAR
Direct HF hadron measurements (p+p and Au+Au)
  (1) Heavy-quark cross sections: D0±*, DS, ΛC , B, …
  (2) Both spectra (RAA, RCP) and v2 in a wide pT region: 0.5 - 10 GeV/c
  (3) Charm hadron correlation functions, heavy flavor jets
  (4) Full spectrum of the heavy quark hadron decay electrons
Physics
  (1) Measure heavy-quark hadron v2, heavy-quark collectivity, to study the medium properties e.g. light-quark thermalization
  (2) Measure heavy-quark energy loss to study pQCD in hot/dense medium e.g. energy loss mechanism
  (3) Hadro-chemistry including heavy flavors
Notes: Need to go through formatting

## Slide 10: DCA resolution performance r-ϕ and z
GEANT: Realistic detector geometry + Standard STAR tracking
including the pixel pileup hits at RHIC-II luminosity
Goal with Al-based cable (Cu cable -> 55 micron for 750 MeV/c K)
10
0.4% X0

## Slide 11: Physics – Run-14,15 projections
RCP=a*N10%/N(60-80)%
Assuming D0 v2 distribution from quark coalescence.
1 B Au+Au m.b. events at 200 GeV.
- Charm v2 
Medium thermalization degree
Drag coefficients!
Assuming D0 Rcp distribution as charged hadron.
1B Au+Au m.b. events at 200 GeV.
Charm RAA 
Energy loss mechanism!
Color charge effect!
Interaction with QCD matter!
Notes: Possible add in the RAA for D0 in AA (as shown before – to illustarte how it can be done)

## Slide 12: B tagged J/
Prompt
J/ from B
Current measurement via J/-hadron correlation have large uncertainties.
Combine HFT+MTD in di-muon channel
  Separate secondary J/ from promptJ/
  Constrain the bottom production at RHIC
STAR Phys. Lett. B 722 (2013) 55..

## Slide 13: HFT Project Status
HFT upgrade is nearing completion after a 3 year construction period
All detector components have passed the initial testing, integration and commissioning has begun
The full assembly including PXL, IST and SSD will be available for RHIC Run-14, which is planned to be a long Au-Au run