## Slide 1
Qiu Hao (LBNL)
for the STAR Collaboration
STAR Heavy Flavor Tracker

## Slide 2
2
Outline
Physics motivation
Design
  Heavy Flavor Tracker
  PiXeL detector
  Monolithic Active Pixel Sensors
Status and performance
  Status
  Signal, pedestal and noise scan
  Efficiency
  Survey and alignment
  Hit residual and track DCA
Summary
Qiu Hao

## Slide 3
3
Physics Motivation
Heavy flavor
  mb,c >> TC, ΛQCD, mu,d,s
  Produced early in initial hard scatterings Good probe to QGP
  Total number conserved in system evolution at RHIC
However, it’s also difficult to study heavy flavor quarks in experiments
  Limited yield comparing with light flavor particles
  Large combinatorial background for direct reconstruction of open heavy flavor hadrons without displaced decay vertex reconstruction
  Large kinematics smearing for studies with electrons from semi-leptonic decay
A precision vertex detector will be an important tool to asses HF physics.
Qiu Hao

## Slide 4
4
HFT can be used to study heavy flavor production by reconstruction of displaced decay vertices
  D0 → K- π+
    BR = 3.83 % cτ ~ 120 μm
  → p K- π+
    BR = 5.0 % cτ ~ 60 μm
  B mesons → J/ψ + X or e + X
    cτ ~ 500 μm
How Heavy Flavor Tracker Helps
without HFT
arXiv:1404.6185
simulation with HFT
s/(s+b) = 0.0001
Qiu Hao

## Slide 5
5
projection of D0 RCP with HFT
Total charm yield baseline for charmonium suppression & coalescence
RCP, RAA energy loss mechanism, QCD in dense medium
Charm collectivity degree of light flavor thermalization
Low radiation length enables reconstruction of D0 down to very low pT, enabling more direct and precise measurement of total charm cross section and charm flow.
Separating charm and beauty probing the medium with heavy quarks with different mass
Examples of Physics with HFT
projection of D0 v2 with HFT
simulation of separating prompt and B decayed J/ψ with HFT
Qiu Hao

## Slide 6
HFT in STAR
6
Tracking & dE/dx:
Time Projection Chamber
Particle ID:
Time Of Flight detector
Heavy Flavor Tracker (run 14)
Electromagnetic Calorimetry:
Barrel EMC
+Endcap EMC
Muon Telescope Detector (runs 13/14)
Full azimuthal particle identification at middle rapidity
Qiu Hao

## Slide 7
7
Intermediate Silicon Tracker:
single-sided double-metal silicon pad
sensors with 600 μm × 6 mm pitch
σr-φ: 170 μm σz: 1800 μm
radius: 14 cm X/X0 < 1.5 %
See details at poster M-30 by Yaping Wang
The task of SSD and IST is to guide the track from TPC to the innermost PXL detector with high hit density.
Silicon Strip Detector:
existing detector with new faster electronics
double sided silicon strip modules with 95 μm pitch
σr-φ: 20 μm
σz: 740 μm
radius: 22 cm
X/X0: 1 %
HFT Design
Qiu Hao

## Slide 8
8
Pixel Detector Design
PIXEL detector
10 sectors * 4 ladders (1 inner + 3 outer) * 10 Monolithic Active Pixel Sensors
  20.7 μm pixel pitch
  thinned down to 50 μm
  used in a collider experiment for the first time
light carbon fiber support
radius:
  2.9 cm (inner)
  8.2 cm (outer)
σ:
= 7.8 μm vibration
X/X0: 0.4 % / layer
360 M pixels in total
air cooled
3 kinematic mounts locate the PXL half on the PXL supporting tube.
xyz constraint
xy constraint
x constraint
PXL insertion can be done in ~12 hours, by pushing PXL halves along rails and latching on kinematic mounts.
2 sets of PXL detectors and 40 spare ladders are made, to replace damaged detector units when needed.
Qiu Hao

## Slide 9
9
MAPS pixel cross-section (not to scale)
Monolithic Active Pixel Sensors
standard commercial CMOS technology
sensor and signal processing are integrated in the same silicon wafer
discriminator & zero suppression in sensor, readout raw hits directly
  integration time 185.6 μs
  Reticle size (~ 4 cm²)
  928 x 960 ~= 890 k pixels
  Pixel pitch 20.7 μm
signal mainly from thermal diffusion in the low-doped epitaxial layer (10~15 μm)
100 % fill-factor
MIP signal < 1000 electrons
collected in large E-field depleted region
Correlated Double Sampling
Qiu Hao
Developed by PICSEL group of IPHC-Strasbourg.
(Marc Winter et al.) Thank you!

## Slide 10
10
a cosmic event a Au+Au 200 GeV event
The full system has been installed for RHIC 2014 running.
Cosmic data were taken for commission, alignment and efficiency studies (before Feb. 9 and whenever there is long time with no beam)
Some detector performance optimization during 14.5 GeV Au+Au run (Feb. 14 ~ Mar. 11)
200 GeV Au+Au data taking with PXL and IST since Mar. 15
SSD is still in commission – SSD and IST are redundant in guiding TPC track to PXL.
HFT Status
Qiu Hao

## Slide 11
11
IST Pedestal
RMS noise
signal to noise ratio ~ 23
Noise data for PXL and pedestal data for IST and SSD are taken at least once per day without beam, to monitor PXL noise rate, hot pixels, and calibrate IST pedestal.
IST signal with MIP
MVP ~ 440 ADCs
See details at poster M-30 by Yaping Wang
Optimize sub-array thresholds in a PXL sensor for noise rate = 2.e-6
Signal, Pedestal and Noise Scan
IST has stable pedestal and RMS level over all channels
5 2.5 0 -2.5 -5 -7.5
threshold with respect to current value (mV)
noise rate
Qiu Hao

## Slide 12
12
layer | inactive units
PXL inner | 14 %
PXL outer | 1 %
IST | 4 %
Z vs. φ of IST hits
Most PXL sensor damages appears to be radiation related damage possibly due to latch up in thinned sensors.
  Minimal or no damage for > 1 month: our operational methods were successful at stopping or greatly reducing the rate of damage.
  PXL and IST are only turned on when collision rate < 55 kHz.
  the full PXL detector resets every 15 minutes
  Latch up thresholds changed from 400 mA to 120 mA above the measured operating current for each ladder
Damage and Remediation
Z vs. φ of hits in PXL inner layer Z vs. φ of hits in PXL outer layer
100 inner sensors in total
Qiu Hao

## Slide 13
13
IST efficiency measured with cosmic ray: hits / projection
~ 95 % at operational threshold / noise
Tuning for including HFT in tracking is going on…
Efficiency
PXL sensor efficiency measured with cosmic ray: hits / projection
Before the detector response optimization and running with the beam
Average = 97.2 %
Low statistics of near horizontal cosmic operational threshold / noise = 5
Qiu Hao

## Slide 14
Survey and Alignment
Coordinate Measurement Machine is used to survey HFT detector parts.
14
PXL sensor surface profile from survey
+- 30 μm > PXL hit error
PXL hit residual distribution before and after PXL half to half alignment
Cosmic ray is used to align different HFT detector parts.
see details at poster M-13 by Michael Lomnitz
Qiu Hao

## Slide 15
Hit Residual and Track DCA
15
IST hit residuals to cosmic track projection: σx = 200 μm, σz = 1800 μm
match IST pad size
DCA resolution for tracks with TPC + 1 IST hit + 2 PXL hits
~ 30 μm at high pT
Below project goal: 60 μm for kaon with pT = 750 MeV/c
PXL hit residual to cosmic track projection after PXL sector alignment: σ < 25 μm, match the design goal
Qiu Hao

## Slide 16
Summary
Qiu Hao
STAR Heavy Flavor Tracker will enable or enhance many open heavy flavor measurements, by reconstructing open heavy flavor hadrons with displaced decay vertices.
State-of-art MAPS technology is used for the first time in a collider experiment in the PXL detector.
All 3 sub-detectors (PXL, IST, SSD) are finished with construction and inserted into STAR before RHIC year 2014 running.
With survey and preliminary alignment, we already achieved ~30 microns pointing resolution for high pT tracks reconstructed with HFT hits.
Data taking with PXL and IST is on a good trend to reach our goal: 1.3 B Au+Au 200 GeV minimum bias events. p+p 200 GeV and more Au+Au data will come in run 15 & 16.
New physics results with HFT will greatly enhance our understanding of QGP created at RHIC.
equivalent goal considering inactive units now
original goal

## Slide 17
Thank you

Qiu Hao