## Slide 1
Catherine Tomkiel, Lehigh University
For the STAR Collaboration
Optical Fibers and Electronics for the STAR Event Plane Detector

## Slide 2: Beam Energy Scan
Key measurements and goals
Location of critical point and first order phase transition
The EPD will improve Centrality and Event Plane measurements, and Triggering
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 3: Overview
Replacement for Beam-Beam Counter (BBC)
Made of plastic scintillator
Two, 1.8m diameter wheels of 12 super sectors each
Each super sector contains 31 optically isolated channels (744 total)
Optical fiber coupled to Silicon Photomultipliers (SiPMs)
Read out by STAR electronics
Super sector
Overview

## Slide 4: Super Sector Construction
Connected to 5.5 meters of clear fiber with 3D-printed custom connectors
Super Sector wrapped in Tyvek and 2 layers of black paper (light tight)
4
Embedded 32-channel
fiber-to-fiber connector
Embedded Wavelength Shifting (WLS) fibers
Clear fibers
A test tile
Super Sector Construction

## Slide 5: Wave Length Shifting Fiber Preparation
Fibers must be polished for optimal coupling
3D-printed custom connectors
Reflective Paint
Reflective Paint on Ends
WLS reflective paint for
“Central Channel”
Decreases cross-talk
WLS Fiber ends painted
Increases light yield by ~30-50%
Catherine Tomkiel, APS DNP October 2017 Meeting
5
5

## Slide 6: Front WLS grooves
3 Loops of WLS per tile
Increases yield by ~2x compared to 1 loop
Central channel and front grooves filled with reflective epoxy
6
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 7: 5.5-m-long Clear Fiber Bundles
Connected to 5.5 meters of clear fiber
  CF attenuation length: >10 m
  WLS attenuation length: >3.5m
CF Connector epoxied together for mechanical stability and light-tightness
Alignment pins
Fiber-to-SiPM
Fiber-to-Fiber
7
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 8
transmission (a.u.)
30 μm
1 μm
80
100
Better polish improves transmission
Correlation between visual inspection and transmission test
8
Catherine Tomkiel, APS DNP October 2017 Meeting
Effect of Polishing on Transmission
fineness of polishing cloth

## Slide 9: Clear fiber bundle meets readout electronics
Fiber-to-Silicon Photomultiplier
connector (FSC)
SiPM
Spacer
Connector
15 ch
16 ch
CF Connector epoxied together for mechanical stability and light-tightness
Alignment pins
9
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 10
EPD SiPM card: 16, 25-μm SiPMs
EPD FSC spacer block
FEE Box
Custom Designed Front End Electronics Card
Clear fiber bundle meets readout electronics
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 11: Read-Out Silicon Photomultipliers – (SiPM)
Clear fiber leads into photosensitive area of SiPM, which digitizes the signal
New technology for hadron colliders – Used in medical technology
  Advantages:
  – No sensitivity to magnetic fields
  – very compact
  Disadvantages:
  – Neutron radiation sensitive
   Placement is important!
11
Catherine Tomkiel, APS DNP October 2017 Meeting
Hamamatsu SiPM:S13360-1325PE
25x25 micron pixels

## Slide 12
beam on (“light current”)
beam off (“dark current”)
Data from pp 500 GeV run
Radiation here is greater than it will be for BES-II
Tile 1, closest to be beampipe
End of run Id~ 1 μA
Operational until Id < ~15 μA
SiPMs good for equivalent of
12 more pp runs
Dark Current Silicon Photomultipliers – (SiPM)
12
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 13
Clear fiber bundles
FEE box
power/control/signal
cables to TUFF & Rx
BBC
EPD/8
13
Catherine Tomkiel, APS DNP October 2017 Meeting
2017 – Quarter Wheel in place at STAR

## Slide 14: Summary
Updated electronics and increased number of channels is an important upgrade for many measurements, including those for BES-II
Data from Run 17 will be discussed by Justin Ewigleben
All super sectors have been constructed: 24 SS plus extra 6 as spares. They are to be installed before Run 18.
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 15: Supersector production
mill isolation grooves (1.65 mm wide) on back ½-way (6 mm deep)
TiO2 + epoxy mixture for isolation grooves, mill the front
  remaining isolation grooves
  WLS fiber grooves (3.5mm), with ramps
epoxy FFC with WLS fibers
optical glue WLS in sigma grooves and central channel
TiO2 + epoxy mixture for front isolation grooves
polish edges, touch-up
wrap
bench tests
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 16: Design
2 Wheels, each composed of 12 supersectors
Each supersector: 31 optically-isolated tiles
1.2-cm-thick scintillator (Eljen EJ-200)
3 turns of WLS fiber (Kuraray Y-11, 1 mmD)
  (3 turns ~doubles light output rel. 1 turn)
Rin=4.5 cm, Rout=90 cm, zmount=375 cm
Each of 12x31x2=744 channels
optical signal transported 5.5 m on clear fiber (Kuraray 1.15 mmD BJ round)
coupled to SiPM (Hamamatsu S13360-1325PE)
  25-μm pixels  1600+ illuminated pixels
read out by STAR FEEs/QTs, similar FPS
Custom-built connector components
3D-printed
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 17: Front isolation grooves
Mill “half-way” and fill groves with TiO2 + epoxy mixture (reflective epoxy)
Optical isolation!
Flip over and finish milling the groves + Fiber channels
17
Catherine Tomkiel, APS DNP October 2017 Meeting

## Slide 18: Fiber bundle construction at Lehigh
Justin Ewigleben
Daniel Brown
Coming to join them:
Catherine Tomkiel, Prashanth
transmission (a.u.)
30 μm
1 μm
fineness of polishing cloth
80
100